ZH Full Color Asynchronous Wifi System User Manual

- Screen Adjust

The default resolution of A300 and A300P is 1024*512, if the LED Screen height less than 512, then just upload content without change; if the height larger than 512, then need adjust the resolution of A300 and A300P; (A100 and A200 default resolution are fixed, so no need do this step)

①Click “Settings--Display Settings”

②Choose “PlayBox”, after the device information refresh finished, click the Setting button below the “Screen parameters”, input password ”168”

③Choose correct resolution (the resolution must larger than the true points of LED screen), click “Set”, after the A300P or A300 reboots, enter this interface again and select sending card in the upper left corner.

④Click receiver card interface, click “Select Module”, choose the module according to your LED board model

⑤Click “Screen Connection”, connect the receiver card in order, then click “Send to Hardware”

After finish these steps, the LED screen will display normal.

- Edit Content

①Change the play window size: Click “Setting---Screen size”, change the width and height, then click “apply”

②Click “New--File Window”, add material

- Upload Content

- U disk Upload Content

①U disk export: click the “Export” button in the top right corner of the software

②Enter the export interface, if you have add time, please click “Time correction”, then click “Export”

③After back up finish, click “ok”, then Unplug U disk

- LAN Cable Send Content

①Click the “send” button in the top right corner of the software

②After the transcoding is completed, the sending interface will pop up, select the corresponding device, and click Send to send the content.

- WiFi send content

Due to information security issues, the factory default WiFi switch is close. Therefore, customers need to connect the network cable to manually turn on the WiFi switch. The steps are as follows:

①Click “Control--Cluster Manager”

②Select device, click “Network Setting”

③Select the wireless network settings, select “Enabled”, confirm the name and password, and click “Setting”.

④Connect to this WiFi signal, to send content.