ZH RGB Text Card Manual

(Mobile APP Operation)

一、Download the software

Please scan the QR code, then will enter into the download page, select the corresponding software version, will show “ Click on the top right corner, Open with Browser ”, then choose the browser to download the software. This software named “ LED Mobile (color) ”, which is compatible with Android, Tablet, iPhone and iPad.

二、Link with WIFI

Enter into the main interface of the software and click “Find” in the lower left corner to enter the WLAN option, connect the WiFi signal which begin with “ZH-M”, the initial WiFi password is 12345678.

- Set the parameter

1、Click“Find”at the lower left corner of the software and enter the device selection interface after search successful. Click the gear icon and enter the password “168” to enter into the screen setting interface.

2、Modify the basic parameters of the display screen, such as: select unit board, height, width, etc., and click “Send”. After sending successfully, the screen display will show the control card model number, version number and other information.

- Edit Content

1、After sending parameters successfully, return to the main interface of the software, click “Now click new”, select device and click “OK”.

- Enter screen name, screen height, width, and so on, then click “OK”. After enter program name click “OK” again.

3、Edit the content, modify the size, font, etc. Click “Send” in the upper right corner.

五、 Modify the default password, click“Find”and “Send” again.

1. After clicking “Send”, the software prompts "modify WiFi password". You can according to the prompt, click "modify WiFi password". After the password is successfully modified, wait for about 2 minutes, connect the WiFi signal again and click “ Find” to search for the device.

- After select the screen and program, and click “Send” in the lower right corner, the screen can normally display the modified content.

Notes:

1. Can the application permissions prompted during software installation be prohibited?

A: Can not.

2. How many devices are allowed to connect simultaneously with the WiFi signal?

A: For security reasons, we allow up to three devices connect simultaneously.

3. Can the WiFi password not be modified?

A: the WiFi password must be modified for security reasons.