LED Video Processor Manual

ZH-Z580

Contents

I. Product Accessories	3

II. Cautions	4

III. Product Description	4

1. Product Features	4

IV. Function Introduction	4

1. Overview	4

V. Panel Diagram	5

1. Front Panel Diagram	5

2. Back Panel Diagram	6

VI. Technical Specification	6

1. Input Criteria	6

2. Output Criteria	7

3. Device Specification	7

VII. Instruction	7

1. Standby Mode	8

2. Main Menu Interface	8

3. Advanced Menu Interface	9

4. FAQ	11

I. Product Accessories

# II. Cautions

(1). Power supply input voltage range: 100~240VAC, 50/60HZ, please use correct power supply.

(2). If you want to connect or unplug any signal wire or control cable, please confirm unplug all power supply cables first.

(3). If you want to add or remove hardware to the device, please confirm unplug signal wire and power supply cable first.

(4). Prior to any hardware operation, please turn off the power supply of LED video processor, and release the static on your body by touching the earth surface.

(5). Please ensure that the using environment is dry, ventilated and clean, and keep the device away from high temperature or moisture environment.

(6). This device belongs to electronic products, please keep away from fire source, water source, and inflammable and explosive dangerous products.

(7). There is high voltage in the device. Nonprofessionals please do not open the case or repair the the device personally. Smoking or odd smell appears, unplug the power switch immediately and contact with dealer.

# III. Product Description

## 1. Product Features

(1). Support the maximum output resolution is 1920*1200, support user-defined.

(2). Support five-channel HD signal input: HDMI, DVI, VGA, CVBS1, CVBS2.

(3). Fade in/out effects, seamlessly switch between different input signals.

(4). Support image adjustment on brightness.

(5). Support EDID manager.

(6). Support dual mode key lock function.

(7). Support built-in 2 pieces sending cards.

(8). Support key, knob multi-mode adjustment.

(9). Standard 1.5U case, standard portable case, convenient for construction and installation.

(10). Power supply voltage input range: AC 100~240V, 50/60Hz.

(11). Support online system upgrade.

## IV. Function Introduction

## 1. Overview

The device ZH-Z580 is a high definition(HD) video processor which is developed for LED large screen display system. It uses leading lossless zoom technique in this industry, supports 2 pieces sending cards inside and cascade in various ways, supports HD DVI/HDMI input and DVI output, and provides LED large screen HD display solutions to customers. Besides fast switching video signal source, the product simplifies the customer operation process which really achieves the minimalistic operation. This device takes the memory processing special for operation interface, which supports standby interface, and interface recovery. The screen is smooth and stable when partial screen and full screen mode freely switching. The device provides multi-mode key lock, and more safe operation choice. Z580 system supports online upgrades which can offer new functions to customers.

## V. Panel Diagram

## 1. Front Panel Diagram

| Switch | Power Supply Switch |
| --- | --- |
| LCD Screen | Display Detailed Operation Tips |
| Knob | Adjust LED Screen Resolution |

| Button Part |
| --- |
| HDMI | HDMI Signal Input Option Key | PART | Part/Full Screen Switch |
| DVI | DVI Signal Input Option Key | MENU | Enter “Advanced Setup” Mode |
| VGA | VGA Signal Input Option Key | OK | Confirm Key |
| CV1 | CV1 Signal Input Option Key | BRI | Brightness Adjust Key |
| CV2 | CV2 Signal Input Option Key | LOCK | Key Lock |
|  |  | BACK | Return to the Previous Menu |

## 2. Back Panel Diagram

| Signal Input Port | Signal Output Port |
| --- | --- |
| HDMI | HDMI Input Port | DVI1 | Output Port 1 |
| DVI | DVI Input Port | DVI2 | Output Port 2 |
| VGA | VGA Input Port |  |  |
| CV1 | CV1 Input Port |  |  |
| CV2 | Cv2 Input Port |  |  |

## VI. Technical Specification

## Input Criteria

| Port | Quantity | Resolution Specification |
| --- | --- | --- |
| HDMI | 1 | EIA/CEA-861 Standard, meet HDMI1.3 Standard |
| DVI | 1 | Support 1920*1080/60Hz and so on, which meet the VESA standard resolution |
| VGA | 1 | Support 1920*1080/60Hz and so on, which meet the VESA standard resolution |
| CV | 2 | PAL/NTSC |

## Output Criteria

| Port | Quantity | Resolution Specification |
| --- | --- | --- |
| DVI | 2 | 1024X768/60Hz 1024X1280/60Hz 1280X720/60Hz 1280X1024/60Hz 1366X768/60Hz 1440X900/60Hz 1600X1200/60Hz 1680X1050/60Hz 1920X1080/60Hz 1920X1200/60Hz Self-defined Resolution (the max width: 1920, the max height: 1536) |

## Device Specification

| Input Power Supply | 100~240V AC, 50/60HZ, 0.3A |
| --- | --- |
| Operating Temperature | 0~45℃ |
| Dimensions | 483 X 247 X 63mm（L×W×H） |
| Weight | 3.0 KG |

## VII. Instruction

Dear users, this Z580 video processor is equipped with a 128x64 pixel blue base LCD display, which display clear menu prompt at each step of the operation, and display standby mode when there is no operation or operation timeout. Based on minimalism, the device sets up extremely simple operation mode. Next is detailed introduction which combine with LCD display menu.

## Standby Mode

Input: Means the current signal channel and the state. When signal is normal, it shows the signal, when signal is abnormal, it displays no signal

Output: Means set the LED screen resolution

Mode: “Full-screen” means display full computer desktop, “part-screen” means display screen capture part

Scene: The mode number of current call scene. If no scene is called, the default is scene 1.

Key Lock: “Menu Lock” means functional key lock, “Full Lock”means all key lock

In the standby interface, if press the RETURN/Back button, can return to the previous operation interface. If there is no operation before entering the standby interface, press the “Menu” button, can  enter into the setup menu.

## Main Menu Interface

In order to achieve more efficient setting, we offer the simple operation mode which just needs setting two parameters to make the larger screen display normal.

| Options | Interface | Setup |
| --- | --- | --- |
| Output Resolution |  | Choose the resolution which is larger than the actual points of LED screen, support user-defined |
| LED Screen Resolution |  | Set the actual width and height of the LED display screen by using the knob |

If setting up normally about the above two parameters, then can finish the basic operation, and meet the basic needs.

## Advanced Menu Interface

In order to meet the various requirements of customers, more options can be set under the advanced menu. Next is the function introduction of the various options in the advanced menu.

| VGA Setup |  | Automatically adjust the VGA screen size, and manually adjust parameters. |
| --- | --- | --- |
| Capture Setup |  | Capture any part screen of the input signal source. |
| Call Scene |  | Call the scene mode have been saved |
| Save Scene |  | Save to current system parameter as scene N |
| EDID Manager |  | EDID settings for HDMI/DVI digital video signals |
| Brightness |  | Screen display brightness adjustment |
| Seamless Switch | Instantly switch; Fade in/out | Screen switching effects |
| Fade in Time | Time customized | Adjust the stay time when picture switch |
| Freeze |  | Freeze the current video |
| LED Test |  | Output black, white, red, green, blue and other colors |
| Key Lock | Menu lock/ Full lock | Lock functional keys/lock all the keys |
| Version | V2.X.X | Display device version |
| Factory Setup | OK/Cancel | If click “OK”, then the device will restore to the default setting parameters. |

## FAQ

In the process of operation, it’s unavoidable to encounter some problems caused by incorrect operation. The following are the problems that users can debugging by themselves. If the following methods don’t work, please do not dismantle the device and contact the distributor in time.

| LCD screen doesn’t work | Confirm the power wire is plugged tightly and the power supply is normal. |
| --- | --- |
| The display of LED screen lack of color | Confirm the input/output signal terminal cables are plugged tightly, and tighten the screws. |
| The screen has black edges | (1). Adjust the output resolution larger than or equal to the LED screen physical pixel size. (2). Setup the computer resolution or EDID resolution to the maximum input resolution. (3). If the above operations don’t work, then enter the graphics card setup interface, adjust the extended display (PROCESSERDVI/ PROCESSERVGA) screen, zoom to full screen. (4). Since this problem is more common on general displays, it also can be solved by Google related problems. |
| The VGA signal display is incomplete | (1). Main Menu --- Advanced Setup --- VGA Setup --- Auto Adjust --- OK. (if the adjustment is still incomplete, then repeat the automatic adjustment process.) (2). Manual adjust parameters like H Start/V Start/ Clock Size and so on. |
| Device connection setting is complete, while appear the black screen | (1). Check if the signal source exists. (2). Switch to full screen mode, if it is normal, please check if the screen capture area is black. |