# ZH USB Card Manual

- Software Download.

- Display Setting.

- Subtitle Edition.

- Software Download.

- . Download Website: www.zhonghangled.com/en.

- . Software Name: LED Control System V5.1.1.15.

- Display Setting.

- . Entrance of display setting.

Click “Setting”, then click “Display setting”, the password is 168.

- . Model.

Please choose your controller model. The controller model is printed on the controller card. If you don’t know, you can open your display and check it or ask your supplier.

- . Width and Height.

Please fill the correct display pixel size in the width and height.

If you don’t know it, you can count the quantity of lamp beads in width and height or ask your supplier.

- . Quick.

If your display is P10, please choose “Conventional P10” in the “Quick”.

If your display is indoor dual color F3.75 or F5, please choose “General Indoor” in the “Quick”.

- . OE Polarity and Data Polarity.

After you change the “Quick”, please keep “OE Polarity” and “Data Polarity” default.

However, if your display happens full light appearence, please change the OE Polarity; if your display happens reverse appearence, please change the “Data Polarity”.

- . Color Mode.

Please choose the right color according to your LED display color.

- . Communication Mode.

If you use U disk, please choose “U disk”.

If you use serial cable, please choose “Serial”.

3. Subtitle Edition.

- . Subtitle(Single Line).

If you only want to display single line, you can click “Subtitle”.  Please click extension to full height and full width.

Then you can edit some texts in the text edition area.

You can change the effect and speed of ‘enter’ and ‘quit’ in the “Special Effect” area. In the speed option,  “1” is the fastest.

If you need running side, you can select it in the “Running side” area.

If you need background, you can select it in the “Background” area.

- . Picture Text(Multiline).

You can click “Multi-line” to open the multiline text edition area.

Meanwhile, you can use animation and form. You can also import your own animation, picture, word or excel.

- . Partition.

You can add several partitions in the screen, like time, subtitle, picture-text, dial and so on.

Please remember not to make them overlap.

The maximum number of partition is 16 pieces.

- . Time.

Click “Time” icon, then you can add time to display. You can choose single line display or multiline display.

- . Dial.

Click “Dial” to set the dial clock. You can select the dial shape, fix the text and set Jet Lag for different time, like Beijing, New Delhi, Jakarta, etc.

- . Preview.

Click “Preview” icon. Then a virtual screen will jump out and you can click “+”  to see it through bigger size.

- . Program.

If you need, you can click “Program” icon add more programs, like program 1, program 2, program 3, etc.

If you need, you can also set program play duration for different program so that your screen will display different things in different time.

- . Sending Data.

If you use U disk to communicate, you can click “U Disk” icon.

If you use Serial cable to communicate, you can click “Send” icon.