ZH-5W2L LED Display Controller

Specification

# Hardware:

| Item | Interface Name | Description |
| --- | --- | --- |
| 1 | Hub Port | Connect hub board |
| 2 | Multi-function Button | 1.Test LED panel 2.Reset to defaults |
| 3 | 5V Power Indicator | Indicating power state |
| 4 | 5V Power Port | Voltage range support 3.2V-5.5V |
| 5 | RTC Button Battery | RTC battery, Voltage 3V |

Parameter:

| PC Software | LED Control System V5.1.15 |
| --- | --- |
| Mobile Phone App | ZH Mobile |
| Pixel | 16*640 32*320 |
| Hub Port | 2*hub12 |
| Communication Port | WIFI |
| Support Module Type | All kinds of single/dual color LED display modules |
| Software Function | Multi-language/Multi-program/Multi-partition |
| Program Number | 65536 programs, 16 partitions for each program. |
| Play Type | Text, Graphic, Animation, Time, Clock, Timer, Temperature. |
| Running Side | Over 10 kinds of running sides, support single partition running side. |
| Clock Display | Digital clock, Analog clock, Positive timing, Negative timing. |
| Memory | 1 MByte |
| Brightness Adjustment | 15 levels brightness, automatically adjust by time. |
| Remote Switch | Support timing turn on/off, turn on/off by software. |
| Working Voltage | 3.2V-5.5V |
| Max Power | ≤0.5W |
| Working Temperature | -30℃~70℃ |
| Secondary Development | Offer development protocol |