ZH-EBOX-200 User Manual

--Poster LED Display Proprietary Control System

Content

I. Hardware Introduction	1

II. Screen Adjust	3

III. Edit Content	8

IV. Upload content	10

1. U disk Upload content	10

2. LAN Cable send content	13

3. WiFi send content	15

V. ZH-EBOX-200 Single Device Sync/Async Switching Operate Instruction	17

VI. ZH-EBOX-200 Multiple Device Sync Operate Instruction	18

# Hardware Introduction

| Item | Name | Function | Note |
| --- | --- | --- | --- |
| 1 | Power input 1 | Connect power supply DC3.3-6V |  |
| 2 | Power input 2 |  |  |
| 3 | Receiver card output port | Connect the first receiver card which controlled by this EBox-200 | Form a loop |
| 4 | Receiver card input port | Connect the last receiver card which controlled by this EBox-200 |  |
| 5 | Synchronous output port | Connect the next device’s sync input | Used for multiple device synchronous |
| 6 | Synchronous input port | Connect PC Gigabit network |  |
| 7 | TF card slot | Install SD card | Expand internal storage |
| 8 | USB port | U disk transmission data |  |
| 9 | Audio port | Connect active speakers for audio output |  |
| 10 | PC network port | Connect PC, 100M communication, used in both screen adjustment and network communication |  |
| 11 | Signal indicator | Red indicator light indicates startup, green indicator light indicates operation | The red light is always on and the green light flashes slowly |
| 12 | Brightness- | Reduce brightness |  |
| 13 | Brightness+ | Increase brightness |  |
| 14 | Test button | Test the LED screen | Test whole LED screen, 13 mode |
| 15 | Sync/asynchronous switch | Switch synchronous/asynchronous |  |
| 16 | Sensor |  |  |
| 17 | 485 interface |  |  |
| 18 | WiFi antenna interface |  |  |

# Screen Adjust

The default resolution is 512*1024, if the LED Screen width less than 512, or height less than 1024, then no need adjust the resolution; if the LED screen width larger than 512, or height larger than 1024, then need adjust the resolution;

①Click “Settings--Display Settings”

②Select “Playbox”, after the device information refresh finished, click the Setting button below the “Screen parameters”, input password ”168”

③Choose correct resolution (the resolution must larger than the true points of LED screen), click “Set”;

Note: after change the resolution, the EBox-200 will restart, after restart, then setting other parameters

④Click receiver card interface, click “Screen Board”, choose the module according to your LED board model.

⑤Click “Screen Connection”, connect the receiver card in order, then click “Send to Hardware”.

After finish these steps, the LED screen will display normal.

# Edit Content

①Change the play window size: Click “Setting---Screen size”, change the width and height, then click “apply”.

②Click “New--File Window”, add material.

# Upload content

## U disk Upload content

①U disk export: click the “Export” button in the top right corner of the software.

②Enter the export interface, if you have add time, please click “Time correction”, then click “Export”.

③After back up finish, click “ok”, then Unplug U disk.

## LAN Cable send content

①Click the “send” button in the top right corner of the software.

②After the transcoding is completed, the sending interface will pop up, select the corresponding device, and click“ Send",  to send ......

## WiFi send content

Due to information security issues, the factory default WiFi switch is close. Therefore, customers need to connect the network cable to manually turn on the WiFi switch. The steps are as follows:

①Click “Control--Cluster Manager”

②Select device, click “Network Setting”.

③Select the " WiFi Setting", select Enable, confirm the name and password, and click “Setting”.

④Click this WiFi signal, to send content.

# ZH-EBOX-200 Single Device Sync/Async Switching Operate Instruction

- Toggle switch to synchronous position, show as the figure:

- Singe Device Synchronous /Asynchronous Diagram:

- Software setup section:

Click “Settings” - “Settings”, select send mode of “Network”, to achieve synchronous display.

# ZH-EBOX-200 Multiple Device Sync Operate Instruction

- Multiple Device Synchronous Diagram

Connection as the figure: The receiving card under each EBox-200 forms a loop, and the asynchronous/synchronous switch always in synchronous state.

2.In software setting, select “Network” to send, to achieve Multi-machine synchronous function.