ZH-YHO Asynchronous Player Manual

Thank you for that you use ZH product.  You are using the best full color asynchronous player.  Now follow me to test and use it.

【Prepare】：Use the computer Gigabit Ethernet (NET) to adjust the LED display well.  Make sure that receiving card parameters and connecting relation have saved in the hardware

【Player Start】：Switch on the player power, after 30 seconds, the red light(run) twinkling means player has started.【The system is loading, please wait for a while】

【Connect】：Unplug the LED display computer net cable and insert it to the player “NET” interface.  Press the button “KEY” for about 5 seconds, when the “status”light is on all the time, it means the receiving card has received the parameters successfully【this step is very important】

【Update the program】：Open the software, click the “setting” first and then click the display “screen size”, set the display pixel (based on the display), and then you can edit the program.

【USB update instruction】：After you finish program edition, click the “file”-----“Export Current Project to USB”----“ok”   (when the video file is large, the transcoding time would be longer, please wait for a moment).  After you have saved it successfully, take the USB out and put it into player USB interface. While the “STATUS” light is twinkling, it means it’s reading the data now. When the “STATUS” light is on all the time, it means that it finishes reading. Then take the USB out and you can play it now.

【WIFI update instruction】：

At first, you should find the wifi name “ZH-YHO-XXXX” in your computer wifi setting, the passcode is 12345.  After you finish your edition, click the “setting”-----“PlayerBox Cluster Manage”, when the cluster manage is open, click the “send”.