ZH-ZX Series Manual

I. Software Download

Please download the software from the official website: www.zhonghangled.com/en

Software named: LED Player V5 ( 5.006.004.001 and the above version ).

This software realizes the data communication connection of the equipment, and realizes the software to set up and control the equipment.

II. Hardware Connection

When debugging, you need to use the computer USB connection with device, and connect the computer's HDMI signal to the device to provide signal source. ( other signal sources are also available, such as DVI, VGA, etc. ), the network cable is connected to receiving card in the LED screen.

## III. Screen Set

1: Open the software, select "Sync Mode" and click "Yes". (this prompt will appear when you first install the software and open it).

- Click “ Setting ”---“ Display settings”

- Select "Send Card", it will refresh automatically if the device is connected.

As the picture shows, if the information displayed within the red line means connect the device successfully (the LCD screen in the device will display "LEDPlayer connected")

- Screen Setting ---- Password 168

- Make sure that at least one signal shows "Signal" in the "Signal Board", and select the corresponding signal source button in the "INPUT " on the front panel of the device ( If button light is always on, indicates it has signal; if flash, indicates without signal ).

First time using this device, please notice the version of receiving card, if need update, please contact with us.

- Click “ Scan Board ”, select the suitable model type.

7. Select "Screen Connection", set the " Scan Board Columns", “Scan Board Rows”, “Width” and “ Height” in “Scan Board Size”, and set network cables in the correct order ( LED screen and computer must be in the same direction ). After the configuration is complete, click "Send to HW”, after the screen is displayed normally, click “Save to HW” is ok.